CHARACTERISTICS

Gelatina SC is a pure food gelatin of animal origin, obtained from the collagen of the connective tissues of pigs. It possesses a high gelling power (Bloom 90-100).

The high surface charge makes it particularly reactive with respect to tannins and also in the fining treatments of musts, wines and vinegars, in combination with Silica Sol and Bentonite.

APPLICATION

The use of Gelatina SC in continuous clarification treatments, such as flotation, must be carried out with particular attention:

- to the hygiene, to avoid microbiological contamination

- to the correct dilution, to avoid over or under dosage

Gelatina SC powder is used in the clarification of fruit juices, ciders and musts.

DOSAGE AND INSTRUCTIONS FOR USE

- Must and juices:  from 5 to 10 g/hl

- Ciders: from 5 to 10 g/hl

Note: it is advisable to perform laboratory fining tests in order to find the best dosage.

Disperse Gelatina SC in water at a temperature> 40 °C and stir to facilitate a quick solubilization. A normal dilution ratio of 1:10 with hot water should be increased up to 1:50 in case the solution has to be subsequently used and kept at ambient temperature conditions.

Notes: carefully  sanitize the containers used and immediately use the Gelatina SC solution so obtained.

COMPOSITION

Food grade gelatin (from swine) in granules.

PACKING

25 kg bag

This product is considered as not harmful and therefore it does not requires a Material Safety Data Sheet (MSDS).

# Text boxes

GELATINA SC

FINING AGENT

REV. 0_021219